CONSTRUCTION TYPES

IA - Concrete walls, floors, roofs, etc.

Examples: High-rise and Group I occupancies, such as, Prisons IB - Concrete walls, floors, roofs, etc.

IB - Concrete walls, floors, roofs, etc.

Examples: Mid-Rise and Group R buildings

IIA - Metal walls, floors, roofs, with one hour plaster and/or drywall

Examples: School Building

IIB - Unprotected and exposed Non-combustible materials such as metal walls, floors, roofs, etc.

Examples: Commercial and Industrial Buildings

IIIA - Constructed with materials that naturally non-combustible in nature with the exception of a roof. These materials include concrete tilt-up, block, with a wood roof with one-hour protection

Examples: Warehouse and Industrial Building

IIIB - Concrete, block, or concrete tilt up construction with exterior walls of noncombustible materials and the interior building elements are of any material permitted within the California Building Code

Examples: Warehouses, Industrial Buildings and in older construction found in cities and counties

IV - Heavy timber, also known as "mill" construction; to qualify all wooden members must have a minimum nominal dimension of 8 inches. Exterior walls shall be of noncombustible materials, and the interior building elements are of solid or laminated wood without concealed spaces.

Examples: Hotel/Lodges, Single Family Homes, and used in high fire areas for 1 hour construction. This Type of Construction is also found in old warehouses

VA - Structural elements, exterior and interior walls are of any materials permitted by the California Building Code with all elements having 1 hour protection

Examples: Newer apartment buildings

VB - Structural elements, exterior and interior walls are of any materials permitted by the California Building Code

Examples: Single Family Homes and Garages

SIZE

The square footage of a proposed building shall be utilized to calculate the plan review and permit fees

OCCUPANCY TYPES

Assembly (Group A) - Places used for people gathering for Entertainment, Worship, and eating or drinking

Examples: Churches, Restaurants (with 50 or more possible occupants), Theaters, Concert Halls, and stadiums

Business (Group B) - Places where services are provided (not to be confused with “Mercantile”

Examples: Banks, Insurance Agencies, Government buildings (including police and fire stations), and Doctor's Offices

Educational (Group E) - Schools and Day Care Centers up to the 12th grade

Factory (Group F) - Places where goods are manufactured or repaired (unless considered "High­ Hazard"

Examples: Factories and Dry Cleaners

High-Hazard (Group H) - Places involving production or storage of very flammable or toxic materials.  Includes places handling explosives and/or highly toxic materials

Examples: Fireworks, Hydrogen Peroxide, and Cyanide

Institutional (Group I) - Places where people are physically unable to leave without assistance

Examples: Hospitals, Nursing Homes, and Prisons

Mercantile (Group M) - Places where goods are displayed and sold

Examples: Grocery Stores, Department Stores, and Gas Stations

Residential (Group R) - Places providing accommodations for overnight stay (excluding Institutional)

Examples: Houses, Apartment Buildings, Hotels, and Motels

Storage (Group S) - places where items are stored (unless considered High-Hazard)

Examples: Warehouses and Parking Garages

Utility and Miscellaneous (Group U) – Others

Examples: Water Towers, Barns, Towers